## Slide 1: Type Airworthiness Safety Assessment (TASA) Workshop Team B

## Slide 2: Workshop Objective
Using the ASPIRE guidance below, develop the Claims-Argument-Evidence sub-claim assigned to your team. When developing the sub-claim, consider the argument that would demonstrate satisfaction of the sub-claim, followed by the evidence required to satisfy that argument.
Note: Other teams will be developing the other sub-claims. These will be discussed in the post workshop wash-up.
Evidence Criteria Definition Evidence within the TASA is provided with a confidence colouring as follows: | 
BLUE | The evidence artefact has been reviewed and that the evidence supports the Claim.
GREEN | The evidence artefact supports the Claim, but there are associated recommendations to address minor shortfalls in the evidence.
AMBER | There is less confidence in the evidence artefact’s ability to support the Claim. This could be as a result of the age of the defined evidence, its review status (i.e. under review or draft) or that review and/or Service experience has presented a minor challenge to its ability to support the Claim.
RED | There is poor confidence in the evidence artefact’s ability to support the Claim. This could be because the evidence artefact is not in place or that review and/or Service experience present a significant challenge to its ability to support the Claim.
ASSC and TASA Claim Grade | Claim Criteria Definition
BLUE | The Claim is substantiated. There is no shortfall and the argument is supported by contemporary, appropriate and sufficient evidence. No elevated Risk to Life.
GREEN | The Claim cannot be met fully. There is a shortfall, but this is fully mitigated by effective controls. No elevated Risk to Life.
AMBER | The Claim cannot be met. There is a shortfall that presents a potential elevated Risk to Life, partially mitigated by additional controls. Duty Holder should be informed.
RED | The Claim cannot be met. There is a shortfall that presents an elevated Risk to Life requiring formal consultation with the Duty Holder.

## Slide 3: SA Structure
PC
The AAR Pod is Acceptably Safe to Operate in-Service to Defined Limits, within its Support Framework
SC1
Type Design is Safe
SC3
AAR Pod can be Operated and Maintained Safely In-Service
SC2
Equipment Contribution to RtL is Known, Assessed and agreed ALARP
SC4
Safety Management System Ensures Safe Practices

## Slide 4
AAR Pod is Acceptably Safe To Operate In-service to Defined Limits, Within its Support Framework
Top Level Claim
As Flown AAR Pod Design is Safe
Sub Claim 1
AAR Pod Equipment Contribution to RtL, is Known Assessed and ALARP
Sub Claim 2
AAR Pod Can be Operated and Maintained Safely In-Service
Sub Claim 3
Safety Management System Ensures Safe Practices
Sub Claim 4
ADS Supports Safe Operation and Maintenance of the Air System
Sub Claim 3.5
AAR Pod Maintenance Schedules Assure Safety in-Service
Sub Claim 3.6
Production and Support Framework is Appropriate to support Safety in the Intended Operating Context and Use
Sub Claim 3.3
Actual Usage Reflects Authorised Limits
Sub Claim 3.2
Operating Parameters and Known Limitations Defined
Sub Claim 3.1
An Effective 2-way Reporting Mechanism is in Place between the DT/TAA and the Operating Community
Sub Claim 3.4
AAR Pod Integrity Management Assures Safety in the In-service Context
Sub Claim 3.7

## Slide 5: Sub Claim 3.1 – Operating Parameters and Known Limitations Defined
Evidence 1
Copy as required

## Slide 6: Sub Claim 3.2 – Actual Usage Reflects Authorised Limits
Evidence 1
Copy as required

## Slide 7: Sub Claim 3.3 – Production and Support Framework is Appropriate to Support Safety in the Intended Operating Context and Use
Evidence 1
Copy as required

## Slide 8: Sub Claim 3.4 – An Effective 2-Way Reporting Mechanism is in Place Between the DT/TAA and the Operating Community
Evidence 1
Copy as required

## Slide 9: Sub Claim 3.5 – ADS supports Safe Operation and Maintenance of the Air System
Evidence 1
Copy as required

## Slide 10: Sub Claim 3.6 – AAR Pod Maintenance Schedules Assure Safety in-Service
Evidence 1
Copy as required

## Slide 11: Sub Claim 3.7 – AAR Pod Integrity Management Assures Safety in the in-Service Context
Evidence 1
Copy as required